1.	To find the first root I ran bisect with limits 0 and 0.5 which converged to 0.3639226269 after 32 iterations and newton with initial guess 0.25 which converged to same value after 4 iterations. For second root I used limits 0.5 and 0.7 with bisect to find value 0.5718029815 after 33 iterations. Newton’s method converged to same value after 4 iterations when given initial guess 0.6.

In general Newton’s method is faster but it’s efficiency is also somewhat more difficult to predict. Bisection method’s use of binary search ensures logarithmic time complexity and it will always find a root in given range. Newton’s method on the other hand requires a good initial guess and for some functions the found root might be quite far from the closest root.

2.	Results with different values of B using reasonable initial guesses are shown below.

x0	B	iterations	result
-0.7	0.1	3	-0.7164258891
-0.5	1	3	-0.5884017765
-0.3	10	3	-0.3264020101
-0.1	100	5	-0.1398945646

When x0=1 first two values of B produce results after 4 and 5 iterations but with greater values of B iteration gets stuck in a loop where we never get an answer. This is easy to understand when looking at plots of g(10) and g(100). Next value of x we get from x=0 is quite far from zero but there g(x) is almost linear which in turn results in next x value being very close to zero.

4.	My function gives results that are compatible with ones from WolframAlpha. For example when given array [1, -6, 10, 3] corresponding to polynomial 3x³+10x²-6x+1 my function outputs these three solutions:
-3.872084 + 0.000000*i
0.269375 + 0.116290*i
0.269375 + -0.116290*i

Makefile can be found in tar archive.